## Slide 1: Copying 10 bytes of data from source address to destination address
LDR r0,=0x20000000 ; Source address
LDR r1,=0x20000050 ; Destination address
LDR r2,=10 ; number of bytes to copy
copy_loop
LDRB r3, [r0] ; read 1 byte
ADDS r0, r0, #1 ; increment source pointer
STRB r3, [r1] ; write 1 byte
ADDS r1, r1, #1 ; increment destination pointer SUBS r2, r2, #1 ; decrement loop counter BNE copy_loop ; loop until all data copied

## Slide 2: Moving the contents from Source to Destination Address
LDR r0,=0x20000000 ; Source address
LDR r1,=0x20000100 ; Destination address
LDR r2,=50 ; number of bytes to copy, also
copy_loop ; acts as loop counter
  SUBS r2, r2, #1 ; decrement offset and loop counter
  LDRB r4,[r0, r2] ; read 1 byte
STRB r4,[r1, r2] ; write 1 byte
BNE copy_loop ; loop until all data copied
By using the loop counter as a memory offset, we have reduced usage of more no of instructions

## Slide 3: Read and store significance of !
LDMIA R0!, {R1, R2, R5 & R7} ; Read multiple registers, R0 update to address after last read operation.
STMIA R0!, {R1, R2, R5 & R7} ; Store R1, R2, R5, R6, and R7 to memory; and update R0 to address after where R7 stored

## Slide 4: 128 Bytes to be copied
LDR r0,=0x20000000 ; Source address
LDR r1,=0x20000100 ; Destination address
LDR r2,=128 ; number of bytes to copy, also
copy_loop ; acts as loop counter
LDMIA r0!,{r4-r7} ; Read 4 words and increment r0
STMIA r1!,{r4-r7} ; Store 4 words and increment r1
LDMIA r0!,{r4-r7} ; Read 4 words and increment r0
STMIA r1!,{r4-r7} ; Store 4 words and increment r1
LDMIA r0!,{r4-r7} ; Read 4 words and increment r0
STMIA r1!,{r4-r7} ; Store 4 words and increment r1
LDMIA r0!,{r4-r7} ; Read 4 words and increment r0
STMIA r1!,{r4-r7} ; Store 4 words and increment r1
SUBS r2, r2, #64 ; Each time 64 bytes are copied
BNE copy_loop ; loop until all data copied

## Slide 5: 64 Bit Addition
LDR r0,=0xFFFFFFFF ; X_Low (X ¼=0x3333FFFFFFFFFFFF)
LDR r1,=0x3333FFFF ; X_High
LDR r2,=0x00000001 ; Y_Low (Y ¼=0x3333000000000001)
LDR r3,=0x33330000 ; Y_High
ADDS r0,r0,r2 ; lower 32-bit
ADCS r1,r1,r3 ; upper 32-bit

## Slide 6: Implementation of FOR LOOP
Total = 0;
for (i=0;i<5;i=i+1)
Total = Total + i;
//Assume “Total” is R0 and “i” is R1; the program can be implemented as
MOVS R0, #0 ; Total = 0
MOVS R1, #0 ; i = 0
loop
ADDS R0, R0, R1 ; Total = Total + i
ADDS R1, R1, #1 ; i = i + 1
CMP R1, #5 ; compare i to 5
BLT loop ; if less than then branch to loop

## Slide 7: Function
function1
SUB SP, SP, #0x8 ; Reserve 2 words of stack ;(8 bytes) for local variables ;Data processing in function
MOVS r0, #0x12 ; set a dummy value
STR r0, [sp, #0] ; Store 0x12 in 1st local variable
STR r0, [sp, #4] ; Store 0x12 in 2nd local variable
LDR r1, [sp, #0] ; Read from 1st local variable
LDR r2, [sp, #4] ; Read from 2nd local variable
ADD SP, SP, #0x8; Restore SP to original position
BX LR
__main
BL function1
stop B stop

## Slide 8: Calling Function from other file
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
EXTERN func
; Start of CODE area
__main
LDR r0,=0x10;
BL func
stop B stop
END

## Slide 9: Called Function-(2x+9)
PRESERVE8
THUMB
AREA |.text|, CODE, READONLY
EXPORT func
func
push {r0}
LDR R2,[r13];
MOVS R3,#2
MULS R2,R3,R2
ADDS r2,r2,#9
STR r2,[R13]
pop {r1}
BX LR
END

## Slide 10: Nested Function

## Slide 11: Main Function
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
EXTERN func
; Start of CODE area
__main
LDR r0,=0x10;
BL func
stop B stop
END

## Slide 12: Code for calling func
PRESERVE8
THUMB
AREA |.text|, CODE, READONLY
EXPORT func
EXTERN func2
func
push{LR}
MOVS R1,#08
BL func2
pop{PC}
END

## Slide 13: func calling func2
PRESERVE8
THUMB
AREA |.text|, CODE, READONLY
EXPORT func2
func2
MOVS r2,#08
BX LR
END

## Slide 14: USING BICS and ORRS to Set the priority register with priority levels.
__main
  ldr r0,=0x20000000
ldr r1,=0xffffffff
movs r2, #0xff
lsls r2,r2,#16
bics r1,r1,r2
movs r2, #0xc0
lsls r2,r2,#16
orrs r1,r1,r2
str r1,[r0]
stop b stop
end
The 4 priority register levels are
1.00
2.40
3.80
4.C0
When we are require to set interrupt priority level with 00 having higher priority and CO having lowest priority into a register mapping to a particular interrupt, we use this code.

## Slide 15: BIC (Logical Bitwise Clear)

## Slide 20: SWITCH
;CASE BRANCHING PRESERVE8 ; Indicate the code here preserve ; 8 byte stack alignment THUMB ; Indicate THUMB code is used AREA |.text|, CODE, READONLY EXPORT main ; Start of CODE area
__main
LDR R0, =0
CMP R0, #3 ; Compare input to maximum valid choice
BHI default_case ; Branch to default case if higher than 3
MOVS R2, #4 ; Multiply branch table offset by 4
MULS R0, R2, R0 ; (size of each entry)
LDR R1, =BranchTable ; Get base address of branch table(0x284)
LDR R2,[R1,R0] ; Get the actual branch destination
BX R2 ; Branch to destination
ALIGN 4 ; Alignment control. The table has
BranchTable ; to be word aligned to prevent unaligned read ;

## Slide 21: Continued Switch
table of each destination address
  DCD Dest0
  DCD Dest1
  DCD Dest2
  DCD Dest3
  default_case
  stop B stop ; Instructions for default case
  Dest0 ldr r0, =10
  stop1 B stop1 ; Instructions for case ‘0’
  Dest1 ldr r0, =20
  stop2 B stop2 ; Instructions for case ‘1’
  Dest2 ldr r0, =30
  stop3 B stop3 ; Instructions for case ‘2’
  Dest3 ldr r0, =40
  stop4 B stop4 ; Instructions for case ‘3’
  END

## Slide 24: RORS

## Slide 25: LSLS and LSRS
For logical shift operations, the instructions are LSL (Figure 5.4) and LSR (Figure 5.5).

## Slide 26: Extraction of data value with W bits wide and P is the starting position

## Slide 27: Clearing the bits starting position P and width of the field being W

## Slide 28: Extracting and Clearing the bits starting position P and width of the field being W

## Slide 29: ASR

## Slide 30: ASR
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
; Start of CODE area
__main
LDR r2,=0x00000080;
ASRS r0,r2,#04
LDR r2,=0x80000000;
ASRS r0,r2,#04
stop B stop
END

## Slide 33: LSLS
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
; Start of CODE area
__main
LDR r0,=0x80000001;
LSLS r2,r0,#01
LDR r0,=0x80000001;
LSLS r2,r0,#02
stop B stop
END

## Slide 36: LSRS
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
; Start of CODE area
__main
LDR r0,=0x80000001;
LSRS r2,r0,#31
LDR r0,=0x80000001;
LSRS r2,r0,#30
stop B stop
END

## Slide 39: RORS

## Slide 40: RORS
PRESERVE8 ; Indicate the code here preserve
; 8 byte stack alignment
THUMB ; Indicate THUMB code is used
AREA |.text|, CODE, READONLY
EXPORT __main
; Start of CODE area
__main
LDR r0,=0x80000001;
MOVS r2,#31;32-1
RORS r0,r2
LDR r0,=0x80000001;
MOVS r2,#30
RORS r0,r2
stop B stop
END

## Slide 43: BIC (Logical Bitwise Clear)